## Slide 1: Electrical

## Slide 2: Computers
Main Computer
  Intel i7 processor
  6GB RAM
  USB, Firewire, Serial
Microcontrollers
  The design of a custom daughter allowed us to replace the previous 4 arduinos that responsible for motor control and encoder reading with a single arduino.
  A second arduino is used for controlling lights and various other ancillary systems on the robot

## Slide 3: Sensors
Reused Sensors
LIDAR
  SICK
GPS
  NAV200
New Sensors
Stereo Camera
  Bumblebee2
9 DOF IMU
  Ardupilot
Encoders
  US Digital

## Slide 4: Power
Source
  2 12v lead-acid batteries
  Total energy capacity of 1052 Watt-Hours
  ~1 Hour of motor run time
Distribution
  3 different voltage rails
    24v, 12v, 5v
    First two provide power to sensors and motors
    Last of these provides power to USB hub

## Slide 5: Daugter Board

## Slide 6: Software

## Slide 7: Overview
Summary of this year's work
Architecture
Major Algorithms
  Vision
  Mapping
  Path Planning
  Controls
  Sensor Integration

## Slide 8: This year's work - All new everything
This year's software team had 0 returning members.
The existing codebase had been used and modified over the course of approximately 5 years.
Additionally, the existing codebase was formed around a purely responsive system. Future competitiveness would require transitioning a more sophisticated approach
Solution: Complete Rebase

## Slide 9: Architectural Approach
The first major task we faced was attempting to decide on an overarching approach to creating the software system necessary for the competition.
We wished to follow good object-oriented design principle

## Slide 10: Architecture and Design

## Slide 11: Design
Extensive use of Interfaces and Inheritance to ensure consistency and simplicity.
  All sensor data inherits from a common class providing timing information
Event/Listener design paradigm used to facilitate communication between functional units of the system
  Allowed rapid substitution of algorithms
  System was leveraged to allow for the creation of sensor simulators to allow easy testing in lab.

## Slide 12: Vision
This year's software made extensive use of the OpenCV library
Major Vision Algorithms
  Lane Detection
    Utilizes Lidar data to remove potential distractors
  Visual Odometry
    Uses IMU data to provide update statements over fixed periods of time
    Provides a means of lessening uncertainty present in GPS data

## Slide 13: Path Planning
Our robot employs a version of A* path planning...with a twist.
Normal A* makes the assumption that the robot effectively has a holonomic drive.
To account for this not being the case for most robots, path smoothing algorithms are used to provide more natural motion.
Our modified A* uses more natural robot motions as state changes and a heuristic that penalized time-inefficient decisions such as turning in place.

## Slide 14: Sensor Fusion
The multiple additions of sensors used this year brought with it the question of how to use overlapping and possibly contradicting data.
Our Decision: implement a Kalman Filter
  Brought on additional complexity of trying to determine appropriate parameters for each fused data type.
  Fairly simple for sensors such as GPS
  More complex for alternative data sources such as our visual odometry algorithm